800 MPSCS  INFO

Terms:

- Zone: The State is divided into areas controlled by computers called Zone controllers..  All towers and hard-wired dispatch centers are connected to a  zone controller via microwave or other network connection. KDPS and KCSO gets their connection through Charter Cable and or AT&T T-1's for both dispatch and the Howard St. tower. The Lamont tower is connected by T-1 to the Vicksburg tower and from there to a Lansing area zone controller. The Howard St. tower is connected to the Rockford zone controller via the Crosstown facility.

- Site trunking: Is when a tower loses its connection to the zone controller. Units on the affected tower can  communicate with with each other, but not with units on another tower. A site-trunked tower is an “island”.

- Failsoft: This occurs when thesite controller at the tower site fails. Radio may search for a working tower.

- NCC: Network Control Center – Office in Lansing that can assign event talkgroups, take trouble reports, etc. (888) 554-4622

- Paw Paw radio shop (269) 657-3705

Common Talkgroups:

City: 499Disp, 499 Lein, 499Fire, Tac 1,2,3Notes: KDPS  encrypted.

Township: 395P911 Tac 4,5

County: 39P911, 39Lein, 39Trans, Tac 6,7,  39Fire

OEM:  EM1, EM2

Hospital 39Bron 39Borg

Ambulances 39Life, 39Pride, Medcom5

Critical Care Doctor: MCC5

WMAC: 39WMAC

Kalamazoo interoperability 39COM1

Event talkgroups are used for interoperability between agencies and counties. They are reserved 	through the NCC ahead of time. There is no encryption on event groups.

ICALL  is an 800MHz conventional channel monitored at MSP dispatch centers. ITAC are 	conventional repeaters or simplex. ITAC 2 is used in Kalamazoo County.

Towers:

Plainwell (10)

Vicksburg (11)

Howard St. (36)

Lamont  (41)

Patches: 154.310MHz to 499Fire (KDPS)

154.430MHz to 39Fire (KCSO)

159.420 Repeater to 39P911   (Portage)

154.010 To 39Com1 (PFD)

154.265 To 39Com2 (PFD)